## Slide 1: T A S C S
Midterm Meeting
29 May 2018, Rotterdam
in cooperation with
Professor
Peter Turnbull
and

## Slide 2: Agenda
10.30 Introduction to TASCS project (PS)
11.00 Tour de table of all present
11.15 Introduction on practicalities project
11.30 Presentation research
12.30 Lunch
14.00 Presentation research (continued)
15.00 Coffee break
15.30 Discussion
16.30 Summary
17.00 Any other business

## Slide 3: TASCS: Objective & motivation
Identification & assessment of (non-) technological developments that impact the work load of crew members during work/rest
  AIS, radar, (un)loading schemes, port configuration, stress, type of cargo, water stretch, noise, vibrations, physical equipment, administration, ….
Future proof manning regulation
Notes: Comment:
More specifically the project must provide a common basis to the Social Partners for their engagement in establishing a European manning framework that meets the needs of the sector.
In order to fully reflect the reality of today’s European IWT sector, the social partners would like to have as much feedback as possible, and thus propose to work in a diversified manner:
Part 1 Compilation & analysis of studies – research – publications – sector information already available;
Part 2 A broad consultation organised amongst operators and crewmembers - consisting of paper/online questionnaires as well as in-the-field interviews.
The project will consist of:
- a preparatory phase,
The preparatory phase includes: the launching of the research part of the project through the researcher/consortium – the preparation of the thematic workshops – the preparation of the final conference – preparation of the documents for the different events.
three thematic workshops,
  The main phase will consist of thematic workshops – possible in 3 different countries to get balanced feedback. Topics of the thematic workshops are to be defined at the first Project Steering Committee meeting.
a final conference, and a series of follow-up actions. (publication of a brochure, dissemination of the outcomes, etc.): The final conference will serve to sum up and present the results of the project as well as presenting the brochure.

## Slide 4: Goal & Research Questions of TASCS
Evaluating actual time occupancy and work load of crew for inland ships on 7 different categories
Finding relations/correlations for research parameters
Deriving a method/tool for calculating crew manning more sophisticated / better fitting than existing regulations

## Slide 5: TASCS - Deliverables
Documented proposal for easy to use manning instrument
flexible, transparent, future proof
with options
and easy to enforce
European interconnected waterways
Spring 2017 - End 2018
Concise report

## Slide 6: Goal of this TASCS meeting
Presenting current picture of time occupancy and workload
(Interim) Conclusions from the field study and approaches for the tool
Feedback from the steering group

## Slide 7: Methodology
Defining parameters to group similar ships
Interview guide for standardization of the interviews based on tasks structure

## Slide 8: Observation checklist – ultrashort
Process/ vessel/ load/ organisation/ waterway
Work (to be assessed)
  Planning/ preparing
  Managing (team, ballast, waste, bunkering, ..)
  Sailing/ manoeuvring/ landing/ (un-)mooring/ dredging
  (Un-)loading
  Periodic inspection, cleaning & maintenance
  Administration (customs, logbook, shifts, sailing, ..)
  Handling calamities
  Other (personal hygiene, cooking, handover, waiting, training, ..)
Recovery (to be assessed)
  Shift pattern, when, how much, where, …
Travel/ commuting
Notes: Items all having impact on workload

## Slide 9: Methodology
Field study on board to get a picture of the actual
  Time occupancy and
  Workload
  Parallel activities
  Urgency
  by competences
Evaluation of the interviews and finding correlations

## Slide 10: Methodology
Tasks structure:
  Navigation
  Operation of the craft
  Cargo handling
  Periodic inspection of marine engineering equipment
  Maintenance & repair
  Communication
  HSE/ emergencies
  Entrepreneuring
  Other tasks
  Recovery/ pause
  Travel time

## Slide 11: Parameters of the Research
Ship/Cargo type
Ship size
Operation mode
Sailing area
State of technical equipment

## Slide 12: Vessel visits
Large hospitality
Service oriented taxi services
Shared meals
Trustful information shared

## Slide 13: Organization of visits – our impression
Candidates sometimes not aware, not informed, though very helpful
Some companies not willing to participate
Need to feel free to speak, rarely difficult
High flexibility research partner needed in planning; very helpful organisations
Getting aboard on operational facility sometimes limited by 3rd parties (harbour/ company)
Language proficiency sometimes limiting

## Slide 14: Vessel visits
Navigational conditions during visits
  Daylight (clear visibility)
  Regular up to high water level
  No critical situations

## Slide 15: Vessel Visits – 1. Dry bulk
5 Vessels (+ 2 planned)
Length: 55 … 110 m
Width: 6.6 … 10.5 m
Operation areas: Rhine, Main, Canals (D/B/NL), Weser, Hunte
Operation modes: A1, A2, B

## Slide 16: Vessel Visits – 2. Liquid bulk
5 Vessels (+ 2 planned)
Length: 86 … 125 m
Width: 9.5 … 22.8 m
Operation areas: Rhine, Main, Danube, Elbe, Canals (D/NL), ARA
Operation modes: A1, A2, B

## Slide 17: Vessel Visits – 3. Container
7 Vessels
Length: 85 … 180 m
Width: 9.33 … 17.1 m
Operation areas: Rhine, France, ARA, Zeebrugge
Operation modes: A1, A2, B

## Slide 18: Vessel Visits – 4. Convoys
7 Vessels
Length: 17 … 269.5 m
Width: 9 … 22.8 m
Operation areas: Rhine, Main, Danube, Weser, ARA, Canals(D)
Operation modes: A1, A2, B

## Slide 19: Vessel Visits – 5. Day Trip / Ferries
5 Vessels (+ 1 planned)
Length: 37.2 … 50 m
Width: 4.6 … 20 m
Operation areas: Rhine, Saar, Rhone, Neckar
Operation modes: A1, A2

## Slide 20: Vessel Visits – 6. Cabin
4 Vessels (+ 2 planned)
Length: 114 … 135 m
Width: 11.4 m
Operation areas: Rhine, Main, Danube, Moselle, Maas, Frisian Lakes, Rhone, Seine,
Operation modes: B

## Slide 21: Vessel Visits – 7. Tugs
3 Vessels (+ 1 planned)
Length: 15 m
Width: 4.3 m
Operation areas: Rhine, ARA

## Slide 22: Overview visited vessels
Type Area | Dry bulk vessels | Liquid bulk vessels | Con-tainer vessels | Pushed/ coupl. convoys | Daytrip vessels & ferries | Cabin vessels | Tugs | TOTAL
Rhine & tributaries, incl. canals, incl. France incl. Weser etc. | 6 + 2 | 4 + 2 | 3 (+4) (France, below) | 5 (+2) (Dan., below) | 4 + 1 | 2 + 2 (+1) (Dan. below) | 3(+1?) | 27 +8 (+7 bel.)
Danube |  | 1 |  | 2 |  | 1 |  | 4
France (besides Rhine) |  |  | 4 |  | 1 | 1 |  | 6
TOTAL | 6 + 2 | 5 + 2 | 7 | 7 | 5 + 1 | 4 + 2 | 3(+1?) | 37(+8) (=45)

## Slide 23: Vessel visits / Challenges
Challenges met with organisation and execution of ship visits
8 vessels planned
5 vessels presently missing
  mainly 3-4 tugs
  Shall be dealt with on short notice
  Support needed (contacts)
  Option: substitute tugs by other types
  Results will be maintained/ incorporated

## Slide 24: Preliminary general conclusions I
No ship says more crew on board needed than regulatory required
Some vessels indicate to sail sometimes (on purpose) with less crew than required by regulations and that work processes or safety seem not really affected
Most vessels know strict hierarchy in task allocation and working times (some do intensive cooperation, flexible working times and task allocation)

## Slide 25: Preliminary general conclusions II
Workload limited/ acceptable
  Sometimes higher cognitive workload:
    short duration, low occurrence, low predictability long term
    long duration (e.g. radar navigation during fog / at night etc.)
  Physical workload: mostly static, low intensity, sometimes small peaks

## Slide 26: Preliminary general conclusions III
Future technical developments can influence workload or time for several tasks ( workshops)
Influence of variable route, traffic and vessel characteristics
Working hours dominant in workload & recovery
  24/7: short sleeps (average 4, max 5 hours, if 6h shift)
  time of day

## Slide 27: Preliminary general conclusions IV
Certain (rare) tasks are easier to handle with additional hands e.g.
  handling hoses during (un-)loading tanker
  (un-)mooring XXL volume vessels,
  handling dangerous goods (intermittent tank cleaning) etc.
(Additional) personnel non necessarily on board

## Slide 28: Preliminary approach
Categorizing tasks
  Must be done on board, directly contributing to goal of transporting cargo/ passengers
  usually done on board, supporting the primary processes & tasks, but could be outsourced / automated
  other (more generic) tasks that occur during work, not time-bound

## Slide 29: 1. Navigation (Cat I)
  Time occupancy (0.5 … 100% of shift for Boatmaster)
  during sailing / manoeuvring usually uninterrupted time occupancy
  Absolute navigation times vary (vessel, trip etc)
  Employees: following shift rhythm
  Ship owner: as long as it is allowed by reg. (tendency)
Preparation of journey depending on believed familiarity; mostly implicit & ad hoc via friends
Time occupancy boatman dictated by logistic planning and resulting journey planning; sometimes disturbing recovery
In parallel possible: remote inspection, communication, entrepreneuring, when work load is undemanding; keeps people busy

## Slide 30: 1. Navigation (Cat I)
Work load:
  Moderately (seldom extremly), undemanding
  demanding peaks due to traffic/obstacles
  Peaks rarely coped with by alternation / extra recovery
  reduced sight increases demand
Qualification: patent (boatmaster, helmsman)

## Slide 31: 2. Cargo handling (Cat. I/II)
Time occupancy (1.25 … 25% for Boatmaster, 0.75 … 75% for Boatman)
  During (un-)loading
    Absolute time varies (dep. on cargo/passengers, ship size, local sit.)
  During the voyage/ while cargo is on board
    dangerous goods: moderate/high
    Other cargo: practically no
  Division of work between boatmaster and boatman and care for cargo handled differently
In parallel possible: inspection, communication, entrepreneuring

## Slide 32: 2. Cargo handling
Work load (Boatmaster / Boatman)
  Mentally undemanding except for dangerous goods
  Boatmaster is responsible for stability and structural load
  Physically demanding for e.g.
    barge coupling
    Hatches
    Tank cleaning
    Handling hoses for liquid cargo

## Slide 33: 3. Operation of the craft
Time occupancy (0.5 … 38.5% for Boatmaster, 0.38 … 12.5% for Boatman)
  Ballast water (Cat. I)
  Bunkering (Cat. II)
  Time occupancy varies (dep. on ship type, size etc.) in general: rather short

## Slide 34: 3. Operation of the craft
Work load
  Mentally moderately / extremely undemanding
  Can be physically demanding (e.g. heavy hoses for bunkering)

## Slide 35: 4. Periodic inspections (Cat. II)
Time occupancy varies strongly (2 … 25%)
  Mostly done by the boatman
  Time occupancy in general correlates to the age of the equipment and the “requirements” of the cargo
  In principle can be completely outsourced to service partner (→ predictive maintenance; in development esp. by shipping companies)
  Depending from low/ high precision standard of boatmaster

## Slide 36: 4. Periodic inspections (Cat. II)
Work load: moderately undemanding

## Slide 37: 5. Maintenance & Repair
Maintenance (Cat. II)
Repair (Cat. I/II)
Time occupancy (0.5 … 38% for Boatmaster, 8 … 69% for Boatman)
  In general correlates to the age of equipment part
  Sometimes outsourced to service partner (internal or external)
  Painting is sometimes done, because boatmen are available
  but also depends on demand / standard / preciseness of boatmaster
  Depending from type of cargo (sensitive to dirt)
  Seasonal influences: spring on deck; winter inside

## Slide 38: 5. Maintenance & Repair
Workload
  Mostly moderately undemanding
  Peaks to moderately / extremely demanding

## Slide 39: 6. Communication (Cat. I)
Internal
  Boatmaster
  Short time occupancy, often combined with coffee break
External
  During navigation (as part of navigation)
  limited extent entrepreneuring (owners)

## Slide 40: 6. Communication (Cat. I)
Workload
  In general moderately undemanding (but depending on experience of crew)
  However, in case of foreign languages & crews sometimes quite demanding (e.g. cabin vessels in France with foreign boatmaster)
Perception / Approach
  More communication at critical situations considered reasonable
  Standardized communication ‘tools’, phrases etc. on European level considered reasonable

## Slide 41: 7. HSE / Emergencies (Cat I)
Time occupancy is rather low (1-2 d/y)
Often regular training scheduled
  mostly for employees/shipping companies
In case of emergency
  Full time occupancy
  High demanding
  But very seldom

## Slide 42: 8. Entrepreneuring (Cat. II)
Not relevant for employees (onboard)
Owner operators: Handled on various ways, e.g.
  long term freight contracts
  use of service partners, transport market place
  Member of a cooperative
  ‘outsourced’ to family partner (not counted as crew member)
  Self- done: variable number of hours

## Slide 43: 9. Other Tasks
Time occupancy
  Cooking: up to 3.5h (on / off shift)
  Personal hygiene: appr. 1h (off shift)
  Meals: 1h (off shift)
Studying: only unexperienced crew
Waiting is daily business for boatmen, mostly replaced by some maintenance, additional breaks / ‚hanging around‘
Boatmasters: Waiting times replaced by additional breaks or maintenance

## Slide 44: 10. Recovery / Pause
Shift system
  2 × 6h allows not enough sleep (mostly mode B)
  1½ × 8h leads to alternating day/night shifts (mostly mode A1/A2)
On/off-board time
  long rhythms (e.g. 14/14 or 28/28 days) can lead to family problems
Quality of rest varies
  Noisy bridge lowering installations,
  suboptimal routing/ location cabins, etc.

## Slide 45: 10. Recovery
Ship Owners (owner operators)
  Less holidays
  Younger ship owners are willing to work as much as allowed
  elder ship owners tend to more recreation time, e.g. free weekend

## Slide 46: 11. Travel
Handled quite different
  Can be counted as working or private time
  Some companies require for long travels a night in hotel before boarding,
  Long journeys, e.g. Latvia - Germany

## Slide 47: Preliminary Conclusions
Time occupancy
  Pure navigation: 1 person needed
  Navigation time is limited by fatigue
  Operation time = max. navigation time * number of persons
  Additional personal (1 or more) is needed for specific tasks on specific occasions
  Summing these up, might lead to full day occupancy
  Outsourcing/technical systems might reduce additional occupancy to zero  Workshop

## Slide 48: Preliminary Conclusions
Work load
  Observation: mostly moderately or extremely undemanding
  Certain tasks are moderately / extremely demanding
  However, technical solutions / assistance available

## Slide 49: State of technical equipment
Mixed picture
By far not all options used at present
Vessel age is no indicator for (technical) equipment
Various modernisations during vessel life time
Modernisation is also a question of rentability & financing (and market situation / conditions)

## Slide 50: Legislative Framework (selection)
COUNCIL DIRECTIVE 2014/112/EU of 19 December 2014 implementing the European Agreement concerning certain aspects of the organisation of working time in inland waterway transport, concluded by the European Barge Union (EBU), the European Skippers Organisation (ESO) and the European Transport Workers' Federation (ETF)
Verordnung über das Schiffspersonal auf dem Rhein (RheinSchPersV), ZKR/CCNR
Verordnung über die Arbeitszeit in der Binnenschifffahrt (Binnenschifffahrts-Arbeitszeitverordnung - BinSchArbZV)
BinSchUO 2008, Anh. XI
Verordnung des Bundesministers für Verkehr, Innovation und Technologie über die Mindestbesatzung von Fahrzeugen (Schiffsbesatzungsverordnung), StF: BGBl. II Nr. 518/2004
Danube (Austria): Schiffsbesatzungsverordnung – 518. Verordnung des Bundesministers für Verkehr, Innovation und Technologie über die Mindestbesatzung von Fahrzeugen

## Slide 51: Outlook to future regulation
Manning is based on time occupancy in combination with workload for tasks on board
Depending on technical equipment and/or outsourcing
Working time differs between employees and owner operators

## Slide 52: Qualification
Ship owners have problems to find qualified personnel (Companies have not been asked).
Labour market for additional personnel is limited.
Languages are a notable problem (compare Slide on Communication/Workload above)

## Slide 53: first impression possible draft future tool

## Slide 54: Agenda
10.30 Introduction to TASCS project (PS)
11.00 Tour de table of all present
11.15 Introduction on practicalities project
11.30 Presentation research
12.30 Lunch
14.00 Presentation research (continued)
15.00 Coffee break
15.30 Discussion
16.30 Summary
17.00 Any other business

## Slide 55: Next step: Expert workshop June
Goal: look into future
  Non-technical developments
    Outsourcing to service partners
    Transport demands
    Logistic requirements
    Crew planning requirements
    Legal framework & legislation / enforcement
    Labour market

## Slide 56: Next step: Expert workshop June
Goal: look into future
  Technical aspects
    Improved and additional equipment
    Predictive maintenance
    Assistance systems / (semi-)Autonomous navigation
    Waterway & port infrastructures
  Financing of technical improvement in correlation to savings of personnel

## Slide 57: first impression possible draft future tool
Thank you very much for your attention!
© Picture: DST